## Slide 1: Radio Map Estimation
Presenter: Dong Yang
  Computer Science
  Georgia State University, Atlanta, GA, USA
Nov 5, 2024

## Slide 2: Outline
Background
Technical challenges
Problem formulation
State-of-the-art methods
Our method

## Slide 3: Background: Spectrum needs
5G  6G: higher data rate, lower latency, larger capacity, ubiquitous connectivity
~1980
~2020
~2030
~2000
~1990
~2010
1G
2G
3G
4G
5G
6G
AMPS, NMT, TACS
GSM, GPRS, Edge
CDMA2000, WCDMA, TD-SCDMA
LTE,
LTE-A
New Radio
2.4 Kbps
50 Kbps
300ms
60 Mbps
100ms
300 Mbps
10ms
20 Gbps
1ms
>1 Tbps
10-100us
THz, ISAC, AI

## Slide 4: Background: Needs for spectrum monitoring
cognitive radio (CR)
dynamic spectrum access
Spectrum
  Spectrum holes
tactical networks
passive radio coexistence
self-organizing, path planning
Notes: Space-Air-Ground Integrated Network
Wireless Network Management
UAV Path Planning
Outage Detection
Device Self-Organization

## Slide 5: Challenges: Scenarios of spectrum monitoring
(a) Spectrum occupancy (state detection)
Sx(f ;a)
f
a
(b) Cyclic spectrum
(feature detection/classification)
f
2-D Spatial
+ Freq./time
3-D Spatial
(c) Spectrum cartography
(radio map estimation)
Main challenge: high dimensionality
Notes: For sample collection

## Slide 6: What is radio map
Radio map: radio power as a function of location 𝑣, frequency 𝑓 and/or with time 𝑡 denoted by
2-D Spatial Space
Frequency
2-D Spatial Space
Time Slots
2-D Spatial Space
3-D Spatial Space
  useful for network management, coverage planning, spectrum allocation
Radiomap: https://web.altair.com/winprop-telecom

## Slide 7: Problem formulation: Radio map estimation (RME)
Learning-based (centralized) RME Romero –Kim’2022
Γ : ground-truth radio map
sparse observations
(.)
Building info
mapping (e.g. DNN)
full-scale RME
  Measurements: sparse samples collected by terminal devices/sensors
  No channel information required; whereas ray tracing needs channel models
  RUs make partial observations of the global radio map

## Slide 8: Roadmap estimation: SP versus ML
Model-based signal processing (SP)
from sparse data
Data-driven machine learning (ML)
from abundant data
Cooperative spectrum monitoring over distributed networks
RF environment: measurements = physical model h(spectrum state)
Monitoring task: spectrum state = f (measurements) = h-1(・)
 | SP | ML
Physical model | Assumed known | Unknown
Training | Parameters estimation | Data driven
Design variable | Spectrum state | f (.): model parameters
Cooperation | No common spectrum | No common model
Notes: Infer spectrum from measurements, which result from the spectrum state through physical models for the channels and transceivers

## Slide 9: Model-based SP method: LDPL[1]
LDPL model:
Making a parameterized version of a., and assuming only 1 TX and the location of that TX is known:
the unknown (, ) of b. can be solved with the aquations (3),(4),(5):
LDPL [1]: Using a Log Distance Path Loss Model based Interpolation method
M. Lee and D. Han, ”Voronoi tessellation based interpolation method for wi-fi radio map construction,” in IEEE Communications Letters, vol. 16, no. 3, pp. 404-407, Mar. 2012.
(1)
(2)
(3)
(4) (5)
where P(d), , P(d0) denote an estimated RSS at distance d from TX to point, path loss, observed RSS at reference distance d0
[1]
Notes: r_i measures i-th error between observed and pred. w_i is a weighting factor for r_i. let r_i have a different level of importance in the sum.
s_i​ represents the RSS at observed point
Locations with a high RSS will have a smaller weight w_i, making them less influential in the optimization.
The parameter p controls the sensitivity of this weighting. Higher p values would give less weight to locations with strong signals

## Slide 10: Model-based SP method: IDW[2]
Estimated RSS are calculated by the sum of observed RSS multiplied by a normalized weight :
Weight wi is calculated by Euclidean distance:
IDW [2]: Using Inverse Weight Model based Interpolation method
S. -P. Kuo and Y. -C. Tseng, “Discriminant minimization search for largescale rf-based localization systems,” in IEEE Transactions on Mobile Computing, vol. 10, no. 2, pp. 291-304, Feb. 2011.
(1)
(2)
where li is the i-th observed point, vi is the observed RSS from TX at the observed point
where l is the location of estimated point, is system parameter (typically =0.01)
Limitation of Model-based SP method:
Not capturing shadowing effects (buildings)
[2]

## Slide 11: Generative AI with Physics Loss for RME[3]
Unlike Image Recovery
Spectrum coverage follows physical radio propagation principles.
RME-GAN [3]: Customize the physical loss function of conditional GAN for radiomap estimation
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]

## Slide 12: Overall Framework of RME-GAN
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]

## Slide 13: Simulation Results
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]

## Slide 14: Federated Learning for distributed RME [4]
Local input:
  Local sensor sparse RSS
  Sensor mask
  City map
Homogeneous local tasks: RME given sparse sensor data and building info.
Allow overlapping between adjacent regions.
Combine trimmed local outputs for global RME.
Weishan Zhang, Yue Wang, Lingjia Liu, Zhi Tian, “FedRME: Federated Learning for Enhanced Distributed Radiomap Estimation,” in 2024 IEEE 100th Vehicular Technology Conference (VTC2024-fall),2024. （Received）
[4]

## Slide 15: Simulation Results
Trained with sufficient training data (20k training)
Trained with limited training data (1k training)
RMSE vs sensor volume (1000 testing instances)
Comparable RMSE to centralized learning
Outperforming the standalone method.
Apparently outperforms all baselines

## Slide 16: Simulation
Fewer
sensors
More
sensors
Example output of different RME methods (1k training data):
FedRME gives more reasonable estimates, especially around the Tx
Notes: Due to overfitting, cannot find source
Stdaln:

## Slide 17: Physics-inspired distributed RME: Challenge
Challenge: Heterogeneous local tasks: RME only given sparse sensor data and TX location.

## Slide 18
Thank You!