## Slide 1
Essential Elements of VR Headsets:
A Technical Overview

## Slide 2
CONTENT
NO.1
NO.2
Introduction
Hardware
Optics
Displays
Tracking
Chipsets
NO.3
Conclusion

## Slide 3
1

## Slide 4
Introduction
[1] A Comparison of Immersive Realities and Interaction Methods: Cultural Learning in Virtual Heritage, 2019
There are many types of XR devices[1].
Head-Mounted-Display (HMD)
Spatial Augmented Reality (SAR)
Notes: There are many XR devices. Five types: Head-Mounted-Display (HMD), Spatial Augmented Reality (SAR), Hand-Held-Devices (HHD), desktop screen and projection, and Cave Automatic Virtual Environment (CAVE).

## Slide 5
Introduction
[1] A Comparison of Immersive Realities and Interaction Methods: Cultural Learning in Virtual Heritage, 2019
There are many types of XR devices[1].
Hand-Held-Devices (HHD)
desktop screen and projection
Notes: There are many XR devices. Five types: Head-Mounted-Display (HMD), Spatial Augmented Reality (SAR), Hand-Held-Devices (HHD), desktop screen and projection, and Cave Automatic Virtual Environment (CAVE).

## Slide 6
Introduction
Cave Automatic Virtual Environment (CAVE)
Notes: Cave Automatic Virtual Environment (CAVE).

## Slide 7
Introduction
In this slide, I will focus on explaining the working principles of VR head-mounted displays (HMDs).
Chipset
Displays
Optics
Tracking
Ergonomics
Notes: We focus on HMD in this slide.

## Slide 8
2

## Slide 9
Overall
VR hardware consists of several key components that work together to create immersive environments.
Chipset
Displays
Optics
Tracking
Ergonomics

## Slide 10
Optics
Optics in XR devices are essential for focusing and directing light from the small displays to the user's eyes. In VR devices, the most common types of optics are Fresnel lenses, Pancake lenses, and Aspherical lenses.
https://www.reddit.com/r/AR_MR_XR/comments/u4fchj/meta_switchable_pancake_creates_high_resolution/
Pancake lenses
Pancake lenses structure
Notes: Pancake lenses is the most popular.

## Slide 11
Optics
Pancake lenses are lighter and thinner than other types of lenses, but they suffer from low light efficiency and significant image distortion.
https://www.reddit.com/r/OculusQuest/comments/ql4m3p/pancake_lens_vs_fresnel/
Pancake lenses(Left), Fresnel lense(Right)
Notes: Pancake lenses are widely adopted by manufacturers due to their ease of production, light weight, and enhanced image quality.
Fresnel lenses are compact lenses and provide a special design that provides high optical efficiency with minimal distortion.

## Slide 12
Optics
Pancake lenses are lighter and thinner than other types of lenses, but they suffer from low light efficiency and significant image distortion.
https://www.bilibili.com/video/BV1WH4y1B7Xw
Pancake lenses(Left), Fresnel lense(Right)
Notes: Aspherical lenses, while offering superior optical efficiency and the best image quality, are highly complex, difficult to manufacture, expensive, and larger in size.

## Slide 13
Optics
Pancake lenses will introduce distortions and suffer a significant light loss.
https://github.com/Genymobile/scrcpy, https://www.bilibili.com/video/BV1pW421R7Ji
The source image output via ADB
Light loss comparison
Notes: Distortions introduced by these lenses can be corrected through software.

## Slide 14
Optics
In Yole view, Pancake lenses have dominated the market.
https://www.yolegroup.com/product/report/displays-and-optics-for-xreality-2024/

## Slide 15
Optics in AR
AR glasses mostly using Birdbath optics and Waveguides optics.
https://www.yolegroup.com/product/report/displays-and-optics-for-xreality-2024/
Xreal Air 2 Ultra (BB)
Microsoft Hololens 2 & IVAS 1.2(DOE)

## Slide 16
Displays
Displays are the visual interface of a XR device.
The primary display technologies used in XR devices include Liquid Crystal Displays (LCD), Organic Light-Emitting Diodes (OLED), Mini-LEDs (mLED), and Micro-LEDs(μLED)
Notes: Displays are tiny typically ranging in size up to 7 inches.

## Slide 17
Displays
Displays are the visual interface of a XR device.
The primary display technologies used in XR devices include Liquid Crystal Displays (LCD), Organic Light-Emitting Diodes (OLED), Mini-LEDs (mLED), and Micro-LEDs(μLED)
https://www.oled-info.com/oled-vs-microled-technology-comparison
Notes: LCD displays can be very bright to overcome the light loss of optics.

## Slide 18
Displays
Resolution in XR devices is more complex than in traditional 2D monitors, and the most critical metric for image quality is angular pixel density (PPD). PPD is determined by both the resolution and FoV, influencing the overall clarity and immersion.
H
W
FoV

## Slide 19
Displays
Displays also present technical challenges that need to be addressed.
Screen door effect
Foveated rendering
Notes: Displays are tiny typically ranging in size up to 7 inches.
screen door effect
Forveated rendering

## Slide 20
Tracking Systems
The term tracking refers to the process of determining users’ viewpoint position and orientation[1]. Other tracking technologies are not essential for the basic functionality of VR, for example, eye tracking.
https://www.coursera.org/lecture/ar/outside-in-tracking-PplG1
6DoF
Six Degrees of Freedom refers to the six mechanical degrees of freedom of movement of a rigid body in three-dimensional space.
Notes: The tracking system is a key component of modern VR, directly influencing the quality of immersion.

## Slide 21
Tracking Systems
Tracking systems are categorized into outside-in and inside-out approaches.
https://www.coursera.org/lecture/ar/outside-in-tracking-PplG1
Outside-in and inside-out
Notes: Modern tracking technologies increasingly incorporate artificial intelligence (AI), resulting in faster response times and greater accuracy.

## Slide 22
Tracking Systems
Tracking systems face numerous challenges.
Need for real-time, accurate tracking
Limited space for sensors
Efficient utilization of all available sensors
Managing the computational power required for processing
Notes: Qualcomm Snapdragon XR2 can only handle 5 cameras effectively in same time.

## Slide 23
Chipset
Modern mobile devices integrate CPU and GPU into a set of electronic components called a chipset or System on Chip (SoC). Recently, most XR devices have adopted Qualcomm Snapdragon series for their performance and efficiency.

## Slide 24
Chipset
Ensuring high-resolution displays with smooth performance is a key challenge in advancing XR technology.
Significant efforts are being made to fully optimize chipset computing power, enhance chipset capabilities, and make use of external computing resources.
Notes: On one hand, rendering immersive 3D environments in real-time demands significant computational power, which require suffcient computing power on the chipset.This will lead to some issue about heat dissipation, power consumption and so on. On the other hand, maintaining low-latency interactions and spatial tracking requires highly optimized chipset. Ensuring high-resolution displays with smooth performance is the key challenge in the advancement of XR technology.

## Slide 25
Research Interest on XR
Design algorithm to overcome distortions introduced by lenses
Enlarge FoV by better rendering algorithm
Real-time 3D rendering optimizations for VR applications
Exploring novel methods for reducing the screen door effect
Spatial mapping and object recognition techniques
Advanced sensor integration for enhanced VR/AR immersion
AI-driven adaptive environments in VR/AR applications
Implementing machine learning to enhance object recognition and tracking
Developing collaborative multi-user mixed reality platforms.
And more…

## Slide 26
3

## Slide 27
Conclusion
This presentation discussed the key components of VR head-mounted displays (HMDs) and introduced key concepts related to them. Following that, I addressed the challenges in VR development and indicated possible research interests in VR.
The future of VR and XR holds incredible potential, but it also presents unique challenges. Thank you for your attention. I’m now open to any questions or discussions.

## Slide 28
THANKS